## Slide 1: ICT03A: Advanced Robotics #2 Frame Transformation
Keitaro Naruse
Email: naruse@u-aizu.ac.jp

## Slide 2: 2D frame transformation

## Slide 3: Motivation: Mapping 動機: 地図生成
Frame := Coordinate system フレーム= 座標系
Suppose we detect and measure an object in a robot frame
How do we convert it to world frame in a single step?
This is two-step: rotation（回転） and translation（並進）
XW
YW
OW
XV
YV
OV

## Slide 4: 2D Homogeneous Transformation Matrix 二次元同次変換行列
XW
YW
OW
XV
YV
OV
1-step transformation by homogeneous transformation matrix
It is a special version of Affine transformation
Only translation and rotation
No scale and shear
because we consider only a rigid body

## Slide 5: Matlab Sample Code of 2D Homogeneous Trans. Matrix
function [T] = T2D(x, y, q)
%T2D returns 2D homogeneous trannsformation matrix
% from a target frame to a world frame
% Input
% - x: x coordinate of target x-origin in a world frame
% - y: y coordinate of target y-origin in a world frame
% - q: angle from a world to target frame
% Output
% - T: 3*3 matrix
T = [
cos(q), -sin(q), x;
sin(q), cos(q), y;
0, 0, 1
];
end

## Slide 6: Matlab Sample Code of 2D Homogeneous Trans. Matrix
% Vehicle frame to world frame
X = 6.0; Y = 3.0; Q = deg2rad(60.0);
T = T2D(X, Y, Q);
% Homegeneous points in vehicle frame
pV = [
1, 1, -1, -1; % x
-2, 4, 4, -2; % y
1, 1, 1, 1 % constant
];
% Homegeneous Points in world frame
pW = [ T*pV(:,1), T*pV(:,2), T*pV(:,3), T*pV(:,4)];
% Homegeneous points in vehicle frame
figure(1);
plot(pV(1,:), pV(2,:), 'b+-', pW(1,:), pW(2,:), 'r*-');
xlim([-10 10]); ylim([-10 10]); grid on; pbaspect([1 1 1]);

## Slide 7: Results

## Slide 8: Quiz #1: Frame Transformation in 2D
Suppose a vehicle moves as in the left figure
At each of the positions, it measures the four points from its local frame
Make an integrated map of sensed points with homogeneous transformation matrix

## Slide 9: Example of Result

## Slide 10: 3D frame transformation

## Slide 11: Motivation: Sensor in 3D Space 動機: 3次元空間でのセンシング
Translation in 3D is easy and no problem
However, the orientation in 3D is not so easy
  Roll, Pitch, Yaw angle or Euler angle
  Rotation matrix
  Quaternion
  SO(3): Special Orthogonal Group of 3
3D Homogeneous transformation matrix 3次元同次変換行列
XW
YW
OW
XS
ZW
YS
ZS
Camera
LIDAR

## Slide 12: Roll, Pitch, and Yaw Angle (Variation of Euler Angle) ロール角，ピッチ角，ヨー角（オイラー角）
Represent orientation of two frames by three angles
Roll: f represents a rotation around the x axis,
Pitch: q represents a rotation around the y axis,
Yaw: y represents a rotation around the z axis
Gimbal lock problem

## Slide 13: Euler Angle (Narrow Sense) 狭義のオイラー角
Represent orientation of two frames by three angles
α (or f) represents a rotation around the z axis,
β (or q) represents a rotation around the x′ axis,
γ (or y) represents a rotation around the z″ axis
Gimbal lock problem

## Slide 14: Problem of Euler Angle Representation: Gimbal Lock オイラー角の問題：ジンバルロック
If two axis rotates around the same axis, it loses one degree of freedom
We cannot represent the orientation between the two frames
(Numerical singular point) 数値的な特異点

## Slide 15: Quaternion クオータニオン・四元数
Represent three angles with one real and three imaginary numbers
It is getting popular method and often used in CG
Mathematically stable and no gimbal lock problem
A bit redundant
Not so intuitive

## Slide 16: 3D Rotation Matrix 3次元回転行列
Represent three angles with 3*3 matrix
It is often used in robotics
Mathematically stable and no gimbal lock problem
Redundant representation
Rotation around each axis

## Slide 17: 3D Homogeneous Transformation Matrix 3次元同次変換行列
XW
YW
OW
XS
ZW
YS
XS
RGB-D Cam
LIDAR

## Slide 18
xc
yc
zc
Camera Frame
pV = [
0.32, 0.32, -0.32, -0.32; % u = x
-0.24, 0.24, 0.24, -0.24; % v = -y
1.00, 1.00, 1.00, 1.0; % z = depth
1, 1, 1, 1 % constant
];
World Frame
xW
yW
zW
Camera frame to world one
Rotate around x with 90 deg

## Slide 19: Matlab Sample Code: Main
% Vehicle frame to world frame
Dx = 0.0; Dy = 0.0; Dz = 0.0;
R = deg2rad(-90.0);
P = deg2rad( 0.0);
Y = deg2rad( 0.0);
% Transformatio matrix from camera to world frame
T = HTTrans([Dx; Dy; Dz]) * HTRotZ(Y) * HTRotY(P) * HTRotX(R);
% Homegeneous points in camera frame
pC = [
0.32, 0.32, -0.32, -0.32; % u = x
-0.24, 0.24, 0.24, -0.24; % v = -y
1.00, 1.00, 1.00, 1.0; % z = depth
1, 1, 1, 1 % constant
];
% Homegeneous Points in world frame
pW = [ T*pC(:,1), T*pC(:,2), T*pC(:,3), T*pC(:,4)];
% Display points in vehicle and world frame at the same window
figure(1);
plot3(pC(1,:), pC(2,:), pC(3,:),'b+-', pW(1,:), pW(2,:), pW(3,:),'r*-')
xlim([-3 3]); ylim([-3 3]); zlim([-3 3]);
grid on; pbaspect([1 1 1]);

## Slide 20: Matlab Sample Code: Functions
function [m] = HTRotZ(q)
% HTRotZ(q): returns a homegeneous transformation matirx of rotating an angle of q around Z-axis
m = [cos(q), -sin(q), 0, 0;...
sin(q), cos(q), 0, 0;...
0, 0, 1, 0;...
0, 0, 0, 1];
end
function [m] = HTRotY(q)
% HTRotY(q): returns a homegeneous transformation matirx of rotating an angle of q around Y-axis
m = [ cos(q), 0, sin(q), 0;...
0, 1, 0, 0;...
-sin(q), 0, cos(q), 0;...
0, 0, 0, 1];
end
function [m] = HTRotX(q)
% HTRotX(q): returns a homegeneous transformation matirx of rotating an angle of q around Y-axis
m = [1, 0, 0, 0;...
0, cos(q),-sin(q), 0;...
0, sin(q), cos(q), 0;...
0, 0, 0, 1];
end

## Slide 21
function [m] = HTTrans(t)
% HTTrans(t): returns a homegeneous transformation matirx of translation
% movetion with a column vector of t
m = [1, 0, 0, t(1);...
0, 1, 0, t(2);...
0, 0, 1, t(3);...
0, 0, 0, 1];
end

## Slide 22: Result

## Slide 23: Quiz #2: Frame Transformation in 3D: Frame Conversion from Camera to Vehicle
Vehicle frame
(Turtlebot)
xv
yv
Camera frame
(RGB-D Cam)
xc
yc
zc
zv
Camera has its frame (defined in camera SDK)
Vehicle has another frame (by convention, e.g., moving direction is x)
Camera has attached to vehicle at a height of 1.0 m in the center of vehicle
How do we represent T from camera to vehicle frame

## Slide 24: Quiz #2: Frame Transformation in 3D: Frame Conversion from Vehicle to World
Vehicle moves in world frame
Make a homogeneous transformation matrix from vehicle to world in each vehicle position
xw
yw
xv
yv
yv
xv